## Slide 1: Comprehensive Design Review
  Team 1 (AutoUmp)
  March 9th, 2017
Notes: 30 minutes for ppt + demo
20 minutes for evaluator Q&A
From eval: “Once hardware is selected, estimate performance including communication cost.”
We know we need to update the block diagr
From email from Hollot:
- Provide copies of your presentation slide deck to evaluators.
- Include a clear list of your CDR deliverables.
- Practice your prototype demo, as well as the presentation.
\\\
CDR structure: CDR is comprised of team presentation and prototype demo, evaluator Q&A, and evaluator huddle.
a) Team presentation and prototype demo (< 30 min)
* presentation < 10 min
* presentation and prototype demo may take place in different locations; conference room, SDP lab, other.
* evaluators are silent except for clarifications.
* adviser is silent.
b) Evaluator Q&A’s (< 20 min)
c) Evaluator huddle (after team leaves)
* adviser allowed to briefly comment. Not present thereafter.
* evaluators submit completed CDR evaluation sheets (2 sheets) to course coordinator.
CDR evaluation (see attached sheets. Evaluators will bring a copy of these sheets to CDR): CDR has three evaluated components:
1) Presentation (20%): A power point presentation less than 10min in duration. It contains three parts:
* A succinct overview of the project that demonstrates knowledge of all subsystems, including how they fit together and communicate with each other.
* A brief but complete outline of the upcoming demonstration; i.e., what is working and what is not.
* Clear and reasonable goals for the Final Project Review (FPR). These goals include everything that is needed for a finished, functioning system that meets all its specs.
2) Prototype Demonstration (20%): A demonstration of the functioning prototype. A successful demonstration:
* is professional.
* does not confuse the audience.
* helps the audience understand how the whole system works.
* allows each team member to display an understanding of how his subsystem fits into the integrated system.
* tip: provide a copy of block diagram to all evaluators.
3) Prototype Functionality and Subsystem Integration (60%): A prototype that fully functions:
* all essential subsystems are present and fully integrated with each other.
there is complete, accurate, and appropriate flow of power, data and/or information among all subsystems.
-----------------
From Wolf, a week ago
need to calibrate - look up table for field of view for both cameras
to reduce error
need to create the mount for the sapphire crystals. Also to set up the plate so we can put the cameras/boards in.
watch for distortions resulting from: sapphire being level, camera being tilted
for demo:
show detailed processing: background subtraction
show detailed processing: object detection
for these two, do the ball/pendulum
how do you show the final algorithm? know what the correct answer is, and show that we're finding it?
velcro ball/velcro wall?
Matt: catch and stick
You need to try this out in the space that you'll be demoing in.
For app: show where the ball is? (would need to have both uart and bluetooth set up)
Or can show where the ball is on the computer.
------------------
Is it a brick or does it work? - show data coming out in serial - show denoise, etc. Over serial, at as high a frame rate as possible Would be very nice to show data with actual balls. Video, show swinging ball. Low, left, right, high. Show the bit images. Run them through the algorithm in C, to show we can calculate the correct position. Calibrate, explain the calibration, and use it to obtain accurate reading on your tests. Set of slides that have videos/images that show all this.

## Slide 2: The Team
Justin Marple
CSE
Jason Camiel
EE
Matt Barnes
EE
Timothy Adams
CSE
Notes: - block diagram
- cameras/boards to buy (jason/justin)
- fill in with matlab slides
- put in enclosure (jason)
- android app
- test cases/data collection (jason?)
- cdr deliverables
- timetable
- synchronization figure (barnes' code)
I think the way the matlab code is written and does it's checks- it will never recognize a pitch if the right camera is recording frames earlier than the left camera

## Slide 3: The Problem
Determining strikes and balls without a professional umpire is difficult and inaccurate
Current technology solutions are expensive and require extensive set-up
Incorrectly called pitches lead to angry players

## Slide 4: The Solution
Use a stereo camera and image processing system built into the home plate to determine the baseball’s location
Challenges:
  Time restrictions for bulk of image processing (16.2ms)
  High accuracy required for successful use (~95%)
  Ball detection vs. object detection (e.g. bat)

## Slide 5: Block Diagram - Hardware
Notes: - It may be helpful to show the block diagram before you into a particular component. You can highlight that component on the diagram so that people know what you are talking about.

## Slide 6: CDR Deliverables
Demonstrate complete system functionality
  Implement ball detection, strike zone intersection, and baseball height functions in C (Tim)
  Functioning PCBs (Justin)
  Capable of detecting balls/strikes with hardware at 60fps
Implement full app functionality (Jason)
  2-way Bluetooth communication established
    App receives ball/strike information including XY position of ball
    Plate receives batter height
First iteration of enclosure built (Matt)

## Slide 7: Background Subtraction and Denoise

## Slide 8: Background Subtraction and Denoise

## Slide 9: Background Subtraction and Denoise

## Slide 10: Background Subtraction and Denoise

## Slide 11: Background Subtraction and Denoise

## Slide 12: Object Detection and Find Intersection

## Slide 13: Object Detection and Find Intersection

## Slide 14: Object Detection and Find Intersection

## Slide 15: Object Detection and Find Intersection

## Slide 16: Object Detection and Find Intersection

## Slide 17: Processing Results
(Units in Inches) | Recorded |  | Calculated, Matlab |  | Calculated, C Code | 
Pitch | Width | Height | Width | Height | Width | Height
1 | 0 | 24 | -0.1 | 23.99 | -0.191 | 19.07
3 | 5.5 | 33.75 | 5.4 | 28.2 | 5.72 | 23.09
4 | -3.5 | 31.25 | -2.2 | 27.8 | -2.187 | 20.85

## Slide 18: PCB’s
XMOS PCB
  49mmx49mm 4 layer board
  2000MIPS with 16 cores
  256kB of RAM, 2MB of FLASH
Image Sensors PCB
  26x26mm 4 layer board
  0.65mm BGA pads requiring 4mil trace/spacing
  Stencil was built to aid in the soldering of the BGA

## Slide 19: PCBs

## Slide 20: PCBs

## Slide 21: Low level implementation
Steps:
  Outputs a 25Mhz CLK signal to cameras
  Retrieves a 50Mhz Pixel-CLK signal back from cameras
  Retrieves Horizontal and Vertical sync lines
  Reads 8-bit data bus on falling edge of Pixel-CLK and saves into 32-bit buffer
  32-bit buffer is split into only the “Y” components of “YUYV” format
  Run background subtraction for every pixel

## Slide 22: Low level implementation – difficulties
The XMOS board has horizontal and vertical sync signals are all on the same port
  Each camera needs their own core. Very difficult to share a port event over two cores.
A master thread is used to look for changes on the sync port
  XMOS “channels” are used to communicate when a sync signal changes. Port counters are used to ensure that each core samples their respective camera at the correct time.

## Slide 23: Low level implementation – difficulties
Sync Frame Input pin is used to ensure the PCLK, data-bus, and sync signals are perfectly synchronized
  Knowing one HREF/VSYNC of one camera means we’ll know the HREF/VSYNC of the other
  Critical for running the two cameras together reliably

## Slide 24: Two way Bluetooth communication
Batter height is set per batter within in the app; this data is promptly sent to XMOS
The XMOS drives the app with updates on ball count, strike count, and location
With each set of updated data the app display is changed automatically
In event of error, user may interact with the app to make adjustment or undo; updated data is sent to the XMOS

## Slide 25: UI

## Slide 26: Enclosure
Cameras are placed 13.5 inches apart, tilted 15 degrees to have coverage of the strike zone and surrounding area

## Slide 27: Enclosure
The camera boards are placed on 3D printed mounts that tilt the cameras the desired 15 degrees
The mounts are attached to a single surface to prevent them from rotating relatively to each other
Aluminum sheet (3mm thick) is cut to fit inside outer edge of plate to prevent injuries
Two support ridges are removed from plate to make room for cameras

## Slide 28: Enclosure
30mm holes are cut into the plate slightly less than 13.5 inches apart
  This prevents the “home plate” from blocking the camera’s field of view
34mm sapphire watch crystals will be inserted into a ridge cut 2mm below the top of the hole
The cameras will be mounted so that the lenses are 4mm from the bottom of the lens

## Slide 29: FPR Goals
Code optimized and fully running on XMOS
  Implement filtering algorithm to consistently isolate balls
  Object detection and pitch determination each < ~16ms
Detection accurate, sent to app
  Primary issue, we believe: distortion. Calculate distortion coefficients.
  Report pitch location and determination to app
Complete enclosure
  Insert sapphire crystals
  Update camera mounts/fix to aluminum to create mount that can be secured underneath the plate

## Slide 30: FPR Goals
Code optimized and fully running on XMOS
  Implement filtering algorithm to consistently isolate balls
  Object detection and pitch determination each < ~16ms
Detection accurate, sent to app
  Primary issue, we believe: distortion. Calculate distortion coefficients.
  Report pitch location and determination to app
Complete enclosure
  Insert sapphire crystals
  Update camera mounts/fix to aluminum to create mount that can be secured underneath the plate

## Slide 31: Strike Detection Concept
Locate point in 3D space where ball intersects with the “Strike Zone” plane

## Slide 32: Block Diagram - Software
Notes: - It may be helpful to show the block diagram before you into a particular component. You can highlight that component on the diagram so that people know what you are talking about.

## Slide 33: The Algorithm – Input
Right:
Left:
t
Notes: Right now the left/right images are the same – won’t be the case in the actual presentation
“189 minus 188.png” in Google Drive -> SDP -> Experiments -> Background Subtraction -> Output_Enhanced

## Slide 34: The Algorithm – Background Subtraction
Right:
Left:
Notes: “189 minus 188.png” in Google Drive -> SDP -> Experiments -> Background Subtraction -> Output_Enhanced

## Slide 35: The Algorithm – Filter and Enhance
Right:
Left:
Notes: “189 minus 188.png” in Google Drive -> SDP -> Experiments -> Background Subtraction -> Output_Enhanced

## Slide 36: The Algorithm – Intersection with Strike Zone
Right:
Left:
Notes: Balls will be circled by the MATLAB algorithm.
If balls are on left/right side of center pixel line – cointinue processing. Else, wait. (guaranteed to have this situation if >2 frames is guaranteed)
[“189 minus 188.png” in Google Drive -> SDP -> Experiments -> Background Subtraction -> Output_Enhanced]

## Slide 37: The Algorithm – Find Centroid Pixel
Notes: Image will be replaced by one that Barnes is creating through his MATLAB algorithm, which will have only the two lines that intersect to find the ball

## Slide 38: The Algorithm – Determine Ball Location
Notes: Image will be replaced by one that Barnes is creating through his MATLAB algorithm, which will have only the two lines that intersect to find the ball

## Slide 39: A Word on Synchronization
Notes: Basically – synchronization is not necessary because each camera can calculate the intersection of the ball with the strike zone on its own, shoot that information off to a separate process

## Slide 40: Android App UI

## Slide 41: Indoor Garage testing
Choose aperture and exposure time for outdoor use
Cameras will need to be securely fastened to the plate in addition to each other
Frame rate of 60fps required for accurate testing
Notes: In attempt to do outdoor tests, cameras output were white washed due to aperture
Cameras were fixed to strike zone backboard, which caused movement with ball and rendered most results useless
Streaking ball due to speed of throw for location accuracy.

## Slide 42: Wall Testing
Using two iPhones spread 6 inches apart and defined axis on a cement wall.
Marked and measured pitches using chalk on the wall
The data collected is used to perform validation of the location algorithm
Sources of error that will affect perfect validation include
  Camera movement/angle orientation
  Ball arc between camera and mark on wall a distance of approximately 18 inches.
  Human error in the marking of the position on wall

## Slide 43: Enclosure

## Slide 44: Enclosure Top View

## Slide 45: Power Requirement
Power consumption for processors
  3.7V*0.45A = 1.65W
4 hour game time: 6.75Wh
Charge: 1824mAh
Result: Choose a 2000mAh battery

## Slide 46: Required Parts List
OV7740 Camera Chip (x2)
  60fps
  SCCB Interface
XEF216-512-TQ128 (x2)
  2MB flash
  512kB RAM
  16 cores
OV7440 Lens (x2)
OV7440 Mount (x2)
2000mAh battery

## Slide 47: CDR Deliverables
Demonstrate complete system functionality
  Implement ball detection, strike zone intersection, and baseball height functions in C (Tim)
  Functioning PCBs (Justin)
  Capable of detecting balls/strikes with hardware at 60fps
Implement full app functionality (Jason)
  Pair to plate, complete viewer and umpire views
  2-way Bluetooth communication established
    App receives ball/strike information
    Plate receives batter height
First iteration of enclosure built (Matt)
Notes: Note: CDR 2/27 – 3/10

## Slide 48: Timeline
Complete orders for final system
Design and send out order for PCB
Implement full algorithm in C
Achieve image collection on PCB system
Receive second round of PCB if needed
Bluetooth communication established
App functionality completed
Implement full algorithm in XC
Enclosure completed
Dec 21st
Jan 21st
Feb 21st
Feb 28th
Notes: Note: CDR 2/27 – 3/10

## Slide 49: Demo – Image Collection and Object Detection
Image size: 176x144
Frames per second: 30 -> ~33.3 ms/frame
Limited memory space: can only store two images at a time